The enclosed programs lm4.exe and bc221.exe will generate either the LM or
BC-221 calibration books for those frequency meters lacking such a calibration
book. To generate the calibration book, first you must edit the proper data 
file based on the unit you are calibrating. If you have a LM-1 thru 9, edit
the file "lmcalib.old", entering your data for the indicated frequencies.
If you have a LM-10 thru 22, edit the file "lmcalib.new". Finally for the 
BC-221, edit the file "bc221.dat".  The data for your unit can be obtained 
via several means. 1) Use a frequency counter to measure the units output 
and obtain the corresponding dial settings.  2) Use a known LM or BC-221 to 
obtain the dial setting for the desired frequencies.  3) Use a receiver with 
crystal calibrator to beat the unknown unit frequency against a known 
calibration point. Use a multiple of the units frequency 
(i.e. 130 kc x 10 = 1300 kc) to beat with a known crystal marker 
(i.e. 1300 kc).

After editing the data file with the correct information, rename the edited
"lmcalib.old" or "lmcalib.new" to "lmcalib.dat". Run the program lm4.exe or
bc221.exe to generate the calibration book.  The ".exe" program will generate
a new file called lmcalib.prn (for the LM frequency meter) or bc221cal.prn
(for the BC-221 frequency meter).  Copy the new ".prn" file to your printer 
to obtain the the calibration book for your unit.

The enclosed ".exe" files should run on most IBM or compatable computers.
However, if the files will not run, you may have to recompile them for your 
machine. The necessary Fortran files can be found in the subdirectory
"fortran".  Copy all the files to your own subdirectory. Run "setup.bat" 
and follow the instructions, entering the necessary information relative 
to your machine. The result will be a new ".lib" file tailored for 
your machine.  The necessary fortran source files (lm4.for or
bc221.for) can be found in the appropiate subdirectory "lm4" or "bc221". 
Copy the correct ".for" file into the same directory as the Fortran files. 
Also copy the appropiate ".dat" file from above into the same directory.
To compile the new program, type "for1" at the prompt. You will then be asked 
for the ".for" program name.  Enter "lm4" or "bc221", depending on your unit.
Hit "enter" (or "return") for the next three prompts. You should receive the 
result "No errors" and the DOS prompt. Next enter "for2".  You should receive 
a "No errors found" and the DOS prompt.  Enter "link".  You will then be asked 
for the ".obj" file name, enter "lm4" or "bc221", depending on you program.
Hit "enter" (or "return") for the next three prompts.  At the DOS prompt,
enter "lm4" or "bc221" to run your new ".exe" file.  Assuming you entered
the required data correctly, you will get a new ".prn" file to send to your
printer to generate your new calibration book

The calibration book you generate will not be as accurate as an original
book.  However, the maximum error in the HF range should be less the 0.5 kc
at the ends of the range.  The maximim error in the LF range should be less 
than 50 cycles at the ends of the range. This error is due to a small 
nonlinearity in the capacitor manufacture.  Not bad for a 55 year old design
and 55 year old technology!

Enjoy.  73  Russ Schroeder  W2DYY  9 Feb 96