DIGITRAK 2.8 and 3.6 DOCUMENTATION                    
                          Copyright Larry Curcio
                               24 March 1994

                   SEE ** GETTING STARTED FAST ** BELOW

[See COMPILER NOTES, RUNNING THE PROGRAM (try the exercises), and FIELD
INSTRUCTIONS below]

DESCRIPTION: DIGITRAK is a vertical rocket altitude simulation program (RASP
program) with the following features:

1) Finds altitude and ascent time, and other trajectory statistics from drag
coefficient, diameter, launch mass and engine (i.e.; standard RASP
functions);

2) Finds altitude and drag coefficient from observed ascent time (Temporal
Backtracking);

3) Finds drag coefficient and ascent time from observed altitude (Optical
backtracking);

4) Calculates optimal mass;

5) Supports up to three stages;

6) Supports transonic and supersonic rockets;

7) Two versions: One uses Runge-Kutta method for drag calculation; the other
uses Fehskens-Malewicki. RK may run faster on non-number-crunching machines.
FM runs faster on number-crunchers.

8) Depreciates air density with altitude;

9) Can use drag profiles in prediction and backtracking;

10) Supports staging delays and air starts;

11) Can output GNUPLOT-compatible file with altitude, velocity, acceleration,
and drag coefficient versus time.

12) Input/output in English or metric units.

Thus, DIGITRAK is designed to be used as a practical tool for model and high
power rocket development.

===========================================================================
                        ** GETTING STARTED FAST **
No changes need be made if you are not on TURBO C in DOS, and if you like
English units. In fact, the program may be compiled directly in TURBO C, but
it will have neither color nor true screen clearing.

If you don't like English units, or have TURBO DOS, then DIGITRAK can be
easily adjusted by assigning values to predfined constants. The C language
uses #define statements to do this. These are situated at the beginning of
the program. You can find them with a text editor. 

****** FOR TURBO C IN DOS: look for relvant #define. The correct assignment
is:

#define TURBODOS 1

(DIGITRAK compiles with one warning in DOS TURBO C)
All other operating systems, leave as is. (#define TURBODOS 0)


****** TO CHANGE TO METRIC INPUT, look for relevant #define's. The correct
assignments  are: 

#define ALTUNITS 'M'
#define INUNITS 'M'
#define TEMPUNITS 'C'

Preserve capital/lower case letters in all of the above.

TO COMPILE IN UNIX:
cc digitrak.c -lm -o digitrak

If the program doesn's compile, see COMPILER NOTES below.

DIGITRAK can be adjusted in many other ways, but this is enough for most
people. For other adjustments, (for example, if you are launching from an
altitude other than sea level) see COMPILER NOTES.

===========================================================================
             ****** CHANGES IN VERSION 2.0 ******

o Runge-Kutta method employed. (Slightly faster. Answers are the same.)

o Line deleted from boost procedure, which cause altitude    over-estimation 
 (Previously announced)

o MAXITMASS changed to MAXITMAS, and DELTAMASS changed to DELTAMAS   (Some
compilers cannot take #define's > 8 characters)

o Tabs removed before one set of #if/#else statements.    (Helps keep
compilers happy. My editor snuck them in, honest!)

o Advice to subtract .06 seconds for digital backtracking is deleted.   This
was the result of a bug, the deletion of which is documented    above.

                    ****** CHANGES IN VERSION 2.1 ****** 
o CONTINUOUS TIME: Uses closed-form solutions on last coast time interval.
Without this feature, time is discrete, and intervals must be short. With
this, intervals can be wider, taking better advantage of the R-K algorithm.

o Default coast time interval changed from .005 seconds to .01 seconds for  
faster run-time at virtually no accuracy cost. (DELTAT0 can be changed   
back by the user, if desired.)

o Default tolerance (NEWTTOL) for backtracking is 100 times more exacting.  
this is made possible by continuous time.

                    ****** CHANGES IN VERSION 2.2 ****** 

o FIXED INSUBSTANTIAL BUGS IN CONTINUOUS TIME ROUTINE AND IN MASS
INITIALIZATION. 

o IMPLEMENTED ENGLISH INPUT OPTION (#define INUNITS).

o ALLOWED LAUNCHER > SEA LEVEL (Set #define ALT0 to launch site altitude in
meters). 

o Fixed bug in BACKTRAK_STAGE routine that would bomb on a single stage
rocket
  after an upper stage in a multistage rocket was backtracked.

o Header records in the output file are preceded by '#' to make them
  gnuplot compatible.


                    ****** CHANGES IN VERSION 3.0 ****** 
o Full Fehskens-Malewicki treatment at each interval

o Variable intervals in coast phase.

o Coast phase interval set to 0.1 seconds if SPEED < MACH 0.8  or 
SPEED > MACH 2.0. (Speed out of divergent range)

o Coast phase interval set to .01 seconds otherwise.
(Note that with FM, intervals should not be too short, since machine
precision is more limiting to accuracy than calculational precision after a
point.)


                ** VERSION 3.1 **
     CONTINUOUS TIME EXTENDED TO STAGING DELAYS. THE DEFAULT NUMBER
     OF INTERVALS IN THE BOOST PHASE REDUCED FROM 500 TO 400.

                ** VERSION 3.2 **
     FIXED BUG IN DRAG PROFILE HANDLING PROCEDURE. IMPLEMENTED COLOR
     FOR TURBO DOS. ALSO IMPLEMENTED TURBODOS SWITCH, WHICH SWITCHES
     BETWEEN DOS (#define TURBODOS 1) AND UNIX OR GENERIC
     (#define TURBODOS 0)

                ** VERSION 3.3 **
     OUTPUT FILE FIELDS ARE LABELED. OUTPUT FILE UNITS ARE DETERMINED
     BY INUNITS OPTION. PROGRAM IS BULLET-PROOFED.


                     ****** GENERAL INFORMATION ******
STAGING DELAYS 
Undelayed staging is a technique designed to achieve great velocities. In the
lower atmosphere, this is not the best way to achieve altitude, because
rockets realize diminishing altitude returns to added velocity there. (This
is after a certain velocity has been reached. At low velocities, rockets
actually realize increased returns to added velocity.) It is therefore often
advantageous (in principle) to delay the ignition of an upper stage until the
rocket has slowed down somewhat, but not so long that the rocket comes to a
halt. See warning below!

There are two kinds of delayed staging. In a simple staging delay, the
burned-out lower stage remains attached while the rocket coasts for a time
interval before the next stage is ignited. In what I call an air start delay,
separation occurs at lower stage cutoff, but there is a delay before the next
stage is ignited. The choice of delay type will depend on the relative
ballistic coefficients of the lower and upper stage. 

WARNING! *** READ THIS PARAGRAPH *** The actual effects of staging delays of
either kind cannot be adequately predicted by any simulation program, least
of all a vertical trajectory program. Vertical trajectory RASP programs
assume that all motion is either up or down - this is tantamount to the
assumption of sophisticated active guidance. Staging delays, particularly
those that result in low staging velocities, may cause rockets to veer
radically from vertical trajectories. They may even cause powerdives. This
should be obvious because at low staging velocities, one is effectively
setting off a rocket in the sky without a launch rod. Such untoward results
can be simulated in off-vertical trajectory programs, but they cannot be
reliably predicted by any simulation, since they may be caused or worsened by
unpredictable turbulence or a capricious puff of wind. DIGITRAK prints out
staging velocities to give the user an intuitive idea of a rocket's stability
at staging, however the authors cannot assume any liability in any case.
Staging delays work only in vertical trajectories. In off-vertical flights,
staging delays often result in lost altitude compared to no delays. More
importantly, they usually cause vast increases in the horizontal distances
covered by rockets. 

OPTIMAL MASS CALCULATION 
In a single-stage rocket, DIGITRAK finds the optimal mass straightforwardly.
In a multi-stage context, DIGITRAK assumes that the lower stages are as light
as possible. It then finds the best mass adjustment (positive or negative)
for the highest stage, and adds this adjustment to the mass of each stage
(since the mass of every stage includes the mass of the top stage). This mass
will always be the best possible upper stage adjustment. An undelayed staged
configuration has no feasible optimal launch mass, because the optimal amount
of non-propellant mass in a lower stage (exclusive of upper-stage mass) is
zero. The mass calculated by DIGITRAK will, however, be the *best feasible*
mass for: 

1) All undelayed staged configurations;

2) All 2-stage configurations where an air start delay is used;

3) All N-stage configurations with only one delay that is situated before the
last stage, and is an air start delay;

4) Virtually all practical 2-stage configurations with simple staging delays,
as long as the top stage is not dwarfed by the bottom stage.

The value may be sub-optimal for some odd configurations with simple staging
delays. That is, there may be an attainable non-zero optimal lower stage dead
mass for a rocket with simple staging delays - if the delay is designed to
coincide with a non-negative staging velocity. When this is so, then optimal
mass for the lower stage is less than or equal to what it would have been if
that stage had been the ultimate stage. This is so only when the upper stages
are very small compared to the next lower stage. If the upper stages are
larger than, as large as, or only moderately smaller than the next lower
stage, then the lower stage should be made as light as possible. This is
usually the case in practice.

Globally optimal mass distribution for all delayed configurations is a linear
programming problem, and is not supported in this version, nor are optimal
delay/stage mass combinations. DIGITRAK should be adequate for most
real-world applications.

It may be observed that calculated optimal mass differs somewhat from one
program to another. When this is true, however, it should also be observed
that altitude differences are trivial when the other program's mass value is
substituted. Optimal mass values may also vary slightly with variations in
engine performance, and variations in air density (temperature and humidity).
They are not to be taken as gospel truth, but as good working values. Optimal
mass occurs as a "Knee" in a rocket's altitude/mass curve. 

SPECIAL NOTES ON OPTIMAL MASS: 
o The optimal mass for rockets with Cd=0 (or very small) is the propellant
mass. In other words, the smaller, the better. DIGITRAK will not calculate an
optimal mass for drag coefficients less than .015.

o When optimal mass occurs in the transonic region, there may be more than
one local maximum in the altitude/velocity curve. DIGITRAK may then display
a local maximum that is not the global maximum. Calculations for transonic
and supersonic rockets have limited accuracy anyway. See below.

TRANSONIC AND SUPERSONIC SUPPORT 
Supersonic support is accomplished through the semi-empirical method
described in Mandell, Caporaso, and Bengen Topics in Advanced Model Rocketry.
MC&B use a critical mach number of 0.9. The program as delivered uses an
adjusted formula for a critical mach number of 0.8. To get MC&B's original
formulas, change MCRIT in the function, machmaker to 9. (The compiler option
flags will lead you there. See COMPILER NOTES below.) Unfortunately, the
model assumes zero angle of attack. As rockets approach the speed of sound,
angle of attack oscillates unpredictably. This difficulty is present in every
RASP program supporting transonic and supersonic speeds. If the barrier is
traversed quickly, the errors encountered are tolerable. As of this writing,
there is no totally adequate drag divergence model that can predict angle of
attack variations. (Though the effect of such variations can be modeled
pretty well.)

                            *** COMPILER NOTES *** 
The supplied version compiles cleanly in the UNIX cc and gcc compilers at
CMU. The compile is clean, even when the -Wall (show all warnings) is
selected. 

TO COMPILE DIGITRAK IN UNIX, USE THE FOLLOWING COMMAND LINE:

      cc digitrak.c -lm -o digitrak <return>

This invokes the C compiler (cc), brings it to bear on the source code,
digitrak.c, makes the math library available (-lm), and names the executable
module, digitrak. (-o digitrak) You may name the executable anything you like
by substituting another name after the -o switch. <return> denotes a press of
the "return" (or "enter") key. Do not use upper case letters in the command
line.

DIGITRAK will compile with one warning in DOS TURBO C. (Whenever an
assignment is done in the condition of an if statement, TURBO C gives a
warning. The practice is actually helpful, but it's inelegant.) Set the
switch, TURBODOS to 1 (in #define TURBODOS).

DIGITRAK will compile in WINDOWS TURBO C++, however the contents of
color_routine must be changed or commented out. Also #include <conio.h> must
ve changed or commented out. The TURBO C++ compiler will flag all the
functions with NO PROTOTYPE warnings, but that has no effect on the code..

The source text contains flags that lead the user to places where options may
be tweaked. Look for /*COMPILE OPTION*/ in the text.  There is also a
"Hackers' area," where some things may be changed that most people won't want
to change. Most #defines are documented or otherwise obvious (e.g.; PI).

#if() STATEMENTS These allow decisions to be made at compile time, rather
than at run time. If your compiler does not support these:

1) Put an { at the *end* of each #if() statement;

2) Remove the # from each #if statement;

3) Change all #endif() statements to } 

4) Change all #else statements to } else { statements

5) Look for areas that have #if's around non-executable statements
(#define's). Comment out the inappropriate text.

6) Compile and ignore references to unreachable code, code has no effect, and
to odd comparisons in if statements. The if statements you just generated
compare constants to constants, and this practice worries many compilers.
Most will cope with their worries. Some will even omit the unreachable code
and the always- true conditions for you. In other words, they may function
just like a #if compiler.

                               CUSTOMIZATION
o UNITS OF MEASUREMENT: DIGITRAK allows English or metric input, but you must
configure the program according to your tastes. Here are the relevant #define
settings.
#define INUNITS 'E' for English, or 'M' for metric. BE SURE TO INCLUDE THE
APOSTROPHES IN THE VALUE YOU SET. BE SURE TO USE UPPER CASE. This sets input
dimensions to inches or centimeters, and input mass to ounces or grams.

#define ALTUNITS 'F' for feet, or 'M' for meters. This sets the way you enter
altitude for optical backtracking. (Note that some strange people, like
myself, prefer feet for altitude, and centimeters for rocket dimensions.)

#define TEMPUNITS 'F' for Fahrenheit, or 'C' for Centigrade.

o LAUNCH PAD ELEVATION (altitude): DIGITRAK allows you to define the
elevation of your launch pad. To do this, set #define ALT0 to the elevation
IN METERS. If your club has a waiver in the USA, the elevation of your launch
site will be printed on it in feet. Multiply this number by 0.3048 to get
meters, and put the result in ALT0.

o TURBO C for DOS Adjustment: set #define TURBODOS to 1, otherwise set it to
0. This switch invokes color, screen clearing and screen positioning in TURBO
C for DOS.

or, more generally:

o SCREEN CLEARING, the #define CLS STATEMENT: CLS should be #defined in the
beginning to be the clear screen command for your system. In TURBO C, this is
clrscr(). On UNIX systems this may be defined as whatever clear screen
function prevails. Alternatively you can use printf("\n \n \n \n \n"). You
can use the number of CR/LF's that will actually clear the screen.

o COLOR: If your system has color, DIGITRAK has a function called "Color()",
in which you can write a machine-dependent routine. 


                        THRUST CURVES IN DIGITRAK 
DIGITRAK can be used with thrust curves from SIMLAB, or with thrust curves
converted from the RASP program. The engines are called by the thrust curve
file names. They must all have the type, ".eng", which is NOT to be entered
into DIGITRAK. I made a small program to cut the RASP motor file (in whatever
incarnation) into individual thrust curves. The thrust curves in the motor
file I was using were prepared by Mark Johnson. They are piecewise linear and
made to conform to shape, impulse, and maximum thrust of over 100 motors. I
call the conversion program, MARKURVE.c, for Mark. In addition, all the
individual files put out begin with the letters, mj. 

The program should work directly. Simply compile it, execute it, and give it
the name of the motor file. It will create MANY thrust curves, THEREFORE IT
SHOULD BE RUN IN A CLEAN DIRECTORY. The files all have the type, ".eng". The
letter after the prefix, mj, is the manufacturer ala RASP conventions. The
remaining letters describe the motor itself. Thus:

mjae15.eng is Aerotech E15

mjee15.eng is the Estes E15.


                                RUNNING THE PROGRAM
[SPECIAL NOTE ON MASS ENTRY:
ALL MASSES IN DIGITRAK ARE LAUNCH MASSES. THEY *INCLUDE* MOTOR MASSES
Rocket masses smaller than motor masses will cause abnormal terminations.
THE MASS OF A STAGE *INCLUDES* THE MASS OF ALL UPPER STAGES
Thus, for example, the mass of a first stage is the mass of the entire
rocket.]


Invoke the program by entering:

DIGITRAK

Choose T for temporal backtracking, O for optical backtracking, and P for
prediction (the default - direct simulation from drag coefficient). You may
use upper-case or lower-case letters as you wish. If you wish to backtrack
with using a profile instead of a drag coefficient or shape constant, enter
TP or OP instead of T or O for (respectively) temporal or optical
backtracking with a profile. (Profile backtracking alters trim factor instead
of drag coefficient. Trim factor is a factor by which the entire profile is
multiplied to make it consistent with flight data.)

If T is chosen, then enter the launch mass, engine name, diameter and ascent
time.  If TP is chosen, you must enter the same data and a profile file name
besides. If O is chosen, then enter launch mass, engine name, diameter and
altitude.  If OP is chosen, you must enter these data and the name of a
profile as well. If P is chosen, then enter launch mass, engine file name,
diameter and drag entry. 

A drag entry is one of the following:

1) A drag coefficient. DIGITRAK assumes a drag coefficient has been entered
if the drag entry is a number, and if a non-zero diameter is entered;

2) A shape constant (the sea-level constant by which the square of velocity
must be multiplied to give the drag force). DIGITRAK assumes a shape constant
if the drag entry is a number and if the diameter value is zero; or

3) A drag profile. DIGITRAK assumes a drag profile if the first character of
the entry is non-numeric. A profile is a file of drag constants for each
consecutive integral velocity from 0 m/sec to some large number (<1000)
m/sec. Drag profiles also have information that went into Cd calculation -
including diameter. At this writing, there is no C program for creating these
files. SIMLABV5 has two profile generators that run on IBM clones. These are
being converted. Profiles may take mach effects into account or they may not.
Current profiles do not. They may be corrected for mach effects by DIGITRAK
by concluding the profile entry with /c or /C. Profile file names and file
types must both be entered.

Engine names are the file names (not file types) of engine thrust curve
files. Engine files must have a file type of ".eng". 

When the data are entered, DIGITRAK produces trajectory statistics.  Enter N
to quit, or Y to perform another run.  The values entered on the last run
become the defaults for the next.  This feature is convenient for "What If"
questions.   At the end of each run, the program allows you to compute your
rocket's OPTIMAL MASS, the mass that yields the highest altitude for the
rocket's impulse and drag characteristics.  If you enter 'O' at the prompt,
you will see estimates of your rocket's performance at its optimal mass

Entering N at the end of the run terminates the program. 

Try these configurations for practice:

Configuration #1
1 stage, 100 grams (3.53 oz), mjec6 motor, Diameter=4.16 cm (1.64 inches),
drag coefficient = 0.6.  Altitude will be about 523 feet. Optimal mass is
about 52 grams. Allow the computer to do another calculation. Choose temporal
or optical backtracking. <RETURN> through the input, choosing all the
previous values. The ascent time or altitude from the last run is the default
entry for the backtracking data. Your drag coefficient and altitude should be
extremely close to their previous values.

Configuration #2
2 stages.

Stage #1: 5100 grams (179.9 oz) launch mass, mjik550 motor, diameter=6.5 cm
(2.56 inches), Cd = 0.6

Stage #2: 100 grams (3.53 oz) launch mass, mjec6 motor, diameter=2.48 cm
(.976 inches), Cd = 0.5

Altitude should be about 5163 feet. Optimal mass of first stage is about 5885
grams. For the second stage, optimal mass is about 885 grams (Yes. Because of
the very large first stage, the weight of the upper stage at its optima mass
exceeds its thrust.) Allow the computer to do another calculation, and answer
'yes' when the program asks if you want to keep the optimal mass statistics.
Choose temporal or optical backtracking. <RETURN> through the input, choosing
all the previous values. The ascent time or altitude from the last run is the
default entry for the backtracking data. Your drag coefficient and altitude
should be extremely close to their previous values. Try backtracking each
stage.

Multi-stage Sensitivity Exercises:
o Try changing the drag coefficient of the first stage in the last problem to
1. Does this change make much difference in altitude of the original
configuration - of the optimal mass configuration - of the drag coefficient?
What are the % errors? Does it change optimal mass much? 

o The first stage in this configuration is *much* more powerful than the
second stage. Would you expect a more balanced (and realistic) configuration
to be more or less sensitive to first stage drag coefficient? 

o Make up a realistic configuration to test your answer. Try backtracking
this configuration, using widely varying drag coefficients. What % altitude,
drag coefficient, and optimal mass error do you encounter in the new
configuration? At this point, you should be able to appreciate the note
below.
MULTI-STAGE NOTE: 3-stage rockets are virtually impossible to follow well
enough to backtrack. In practice, most 2-stage rockets can be backtracked by
eyeballing a Cd for the first stage, and backtracking the second stage. Most
such configurations are extremely insensitive to changes in first-stage Cd.
It is wise to check the altitude and drag coefficient sensitivity to the
value of first stage Cd. If the diameters of the stages differ widely then
use an reasonably small value for first stage Cd as a lower bound. To get a
safe lower bound for first stage Cd, and safe upper bounds for second stage
Cd and altitude when diameter is constant, do the following. Backtrack the
second stage with any with any first stage Cd value, then substitute the
backtracked Cd of the top stage for that of the bottom stage, and
rebacktrack. Repeat the procedure until self-consistency is reached. (This is
often reached on the second try, and confirmed on the third.) A safe upper
bound for lower stage Cd is usually unity. The corresponding altitude and
upper stage Cd are good lower bounds for both. The range should be narrow, so
split the difference. The only way to get a good lower stage Cd value is to
launch that stage as a single-stage rocket.


                 FIELD INSTRUCTIONS FOR TEMPORAL BACKTRACKING 
Temporal backtracking is easy to do, but there are many things that one can
do wrong. I myself spent several months believing that temporal backtracking
and RASP programs in general did not work. The belief was based on errors I
had made in the experiments. I have prepared this guide so that others will
not commit the same errors, and reach the same false conclusions about the
method.

0) TAKE TIME TO LEARN THE BACKTRACKING PROCEDURE. Practice on rockets that go
500 feet or less until you have the knack. It helps to verify your learning
by comparing backtracked altitudes with single-station tracking. Altitudes
should compare very well on average. The tendency is to record short times,
at first. Even without tracking verification, this sort of error usually
causes conspicuous underestimates.

1) Always backtrack in calm weather, that is in winds of 7MPH or less. This
is extremely important since high winds cause strong violations of the
mathematical model. Drag coefficients measured on calm days may be used to
predict altitudes in winds up to about 10 MPH (provided weathercocking is
minimal); however they cannot be used to predict parachute delays except in
calm weather.

2) For best results, use large, easily-tracked models. Though experienced
backtrackers can often time highly-visible rockets from near the pad, it is
wise to have timers stationed at distances of at least half the anticipated
altitude of the rocket. Ironically, the farther you are from the launch pad,
the more likely it is that you will not lose sight of the rocket. The more
timers you have, the more chance that at least one of them will be able to
track the model. Since digital stopwatches are inexpensive, there is no
reason why everyone at a launch should not have one.

3) Rocket engines must have the longest delays available. That is, use
upper-stage engines in your single-stage rockets. This is vital. Long delays
guarantee that your rockets will reach their highest points. 

4) Make sure you weigh your rockets on a gram scale. Most schools have
triple-beam balances, which are ideal. Postal scales are not accurate enough.
You may weigh your rockets on the field before launch, or (if they are large
enough so that a gram or two makes negligible altitude difference) you may
weigh them at home or at school. If you do not weigh your rockets immediately
before launch, make certain that they are loaded consistently, so that you
can get an accurate estimate of launch weight.

5) Make certain your launcher is vertical. To do this, hang a beaded metal
chain, of the type used on old electrical pull switches, next to the launch
rod. Adjust the rod until it is parallel with the chain. (Beaded chain is
available at most hardware stores.)

Alternatively, you may wish to tilt your launcher by two degrees. This is
useful when you launch alone, as it causes the rocket to reach apogee some
distance from you while introducing very little error into the backtracking
process. However, though your calculated altitude is likely to be correct, an
off-vertical launch may give you an inflated value for drag coefficient,
since gravity causes the rocket to interact with the air at a non-zero angle
of attack. Also, this method is not suitable should you decide to verify your
backtracking with single-observer optical tracking.

6) Have the person who is launching the rocket give an audible countdown.
Hand signals or whistles are helpful to distant observers. Understand that
there will likely be a short pause between the button push and ignition.

7) Time the rocket's ascent from first *blast* of smoke to the point of
apogee. FOLLOW THE INSTRUCTIONS IN THE SECTION BELOW CALLER _DETERMINING THE
MOMENT OF APOGEE_

8) Average the times from everyone who declares an accurate measurement,
though you should discard wildly inconsistent times from inexperienced
timers.

9) Enter the data in the DIGITRAK program to calculate your altitude.

10) Use average altitude over several flights to calculate your drag
coefficient.


                 *** DETERMINING THE MOMENT OF APOGEE ***
The hardest part of temporal backtracking is the determination of apogee. You
cannot just pick an arbitrary moment in time when the rocket is spatially
near apogee, because it is traveling slowly there, and it spends a lot of
time in the region. Small timing errors translate into altitude errors by
multiplying them times the average speed of the rocket throughout its ascent.
The effects of larger errors are worse. Thus, a second's error typically
translates into about 200 feet of altitude. 

The key to judging apogee is to step back at least half of the rocket's
anticipated altitude. FARTHER IS BETTER. If you are back far enough, you can
see the tracking smoke form an arc at apogee. The successful backtracker
learns to anticipate the formation of this arc and to extrapolate its high
point, so that (s)he can clock the precise moment of apogee. Sometimes the
smoke trail of a rocket will disappear immediately after cutoff. This means
that the rocket is traveling so quickly that its tracking smoke disperses.
The smoke will reappear much higher in the sky, when the rocket slows down.
When you lose a rocket at burnout don't panic. Remember to look for the smoke
trail much higher in the sky. If you still don't see the trail, then look
higher than you had dared. As soon as you see the trail again, you must
extrapolate the arc so you can clock accurately. That is, don't perceive the
smoke trail as a straight line, rather perceive it as the leg of an arc about
to form.

Rockets that fly directly toward you or directly away will sometimes not
reveal an arc; your timing of these will be slightly less accurate. Clock the
point when you just notice that the rocket has nosed over beyond horizontal
attitude. The idea is that, if the rocket goes high enough, it will stray
enough from the vertical to have horizontal velocity at apogee. It is
presumably stable, so it should follow its nose. At its peak, it should be
horizontal, but if you try to clock the point when the rocket is horizontal,
you may be struck by how much "more horizontal" the rocket becomes a moment
later. The moment when the rocket just passes this point is least ambiguous. 

Very low altitude rockets will often not arc over, because they don't acquire
enough horizontal speed. You can usually see such rockets begin to drop, so
clock that moment. There is an additional problem with low altitude rockets,
though. Since they travel slowly, drag has a relatively small influence on
them. I have seen cases when doubling the drag coefficient changes the
altitude no more than 30 feet. Ascent time is also weakly affected. As a
result, drag coefficient is even more sensitive than usual to measurement
errors. Six or seven flights may be required to determine the drag
coefficients of such rockets.


                                    PITFALLS 
1) Rockets travel very slowly near apogee, which is to say they stay around
apogee for a long time. It is not sufficient to time a rocket until it gets
around it's apogee, because it is going to stay within 16 feet of that point
for about 2 seconds. Timing errors translate into altitude by multiplying
them by the average speed of a rocket during its entire flight, not near its
apogee. Nevertheless, there is a tendency to be glib about clocking. CLOCKING
MUST BE PERFORMED RIGOROUSLY, ACCORDING TO THE INSTRUCTIONS ABOVE.

2) Light rockets will often eject just before apogee - even with engines
intended for second stages, as delay times are extremely variable. There is
a tendency to accept data from flights like this because (once again), the
rocket seemed "Almost horizontal." These flights cannot be temporally
backtracked. If you wish to compute a drag coefficient, then weigh these
rockets down with tracking powder.

3) Often a rocket will disappear as it jumps off the pad, only to reappear
again at ejection. There is a tendency to clock this point. There is even a
tendency to perceive this point as apogee. The data in such cases, are
invalid. Discard them. Remember that it is easiest to clock large rockets.

                       MEASURING DRAG COEFFICIENTS (Cd) 
Drag coefficient is often sensitive to errors in backtracking parameters
(time, altitude, engine performance). This is true for both optical and
temporal backtracking. The object is to produce a Cd that delivers an average
altitude for the rocket. In practice, this will vary only slightly with the
backtracking program.

Fly each rocket several times, and compute a mean altitude.  Then backtrack
optically on the mean altitude to get the drag coefficient.  The more flights
you use, the more accurate your Cd is, on average.  Expect performance to
vary from flight to flight, since engine performance varies. Also, random
variations in launch angle, and stability corrections affect your rocket's
angle of attack, and hence its drag characteristics. 

Sometimes rocket masses will vary slightly from flight to flight. In this
case, decide on a standard weight. Backtrack working drag coefficients for
each flight. Using the working drag coefficient, predict an altitude at the
standard launch mass. Use this predicted altitude in your average. Compute
the drag coefficient for the standard launch mass from the average altitude.
Do not use widely different configurations in the computation of a single
drag coefficient, as Cd varies somewhat with speed.

See the MULTI-STAGE NOTE in the exercises at the end of RUNNING THE PROGRAM
for multi-stage backtracking procedures.


                               MEASURING ALTITUDE 
Backtracked altitudes are much more robust than backtracked Cd's are. Average
altitudes are more accurate still. In my own experiments, the average
altitudes of 11 backtracked rockets were correlated at a level of .99 with
average directly-measured altitudes. See the MULTI-STAGE NOTE in the
exercises at the end of RUNNING THE PROGRAM for multi-stage backtracking
procedures.

                                 LIMITATIONS  
BACKTRACKING CANNOT BE PERFORMED IN WINDS GREATER THAN 7MPH, because strong
violations of the simulation model occur in the wind. Temporally-computed
altitudes will be dramatically short in windy weather.  Wind, thus, affects
ascent time more than it affects altitude, taking time preferentially from
low-velocity portions of the trajectory. Fortunately, therefore, drag
coefficients computed temporally in calm weather will predict ALTITUDES
fairly well for winds up to about 10-12MPH; however they will not predict
required parachute delays except for calm weather launches.  No simulation
program will predict performance on windy days.

Rockets must be clearly visible at their apogee. Visibility is usually best
in the morning or late afternoon, and naturally large rockets are easier to
see than small rockets. Visibility is enhanced when viewing from a distance.
Timers should be stationed at least half the rocket's expected altitude from
the launch pad. Longer distances are better. If several individuals are
viewing the launch, and each of them carries a stopwatch, chances are
excellent that at least one of them will follow the rocket to apogee.
Redundant timings should be averaged.

Backtracked rockets should have maximum speeds below mach 0.75.

                                   FINAL NOTE 
Much work has gone into the development of temporal backtracking, and into
the testing and verification of RASP programs. The important results are
merely summarized here. I cannot, however, present an extensive sensitivity
analysis in this document. A detailed account of my experiments is a 93-page
(double-spaced) document.