mkcurve.zip contains mkcurve, awk programs mkcurve.awk and strwac 
and motor files *.raw .

mkcurve invokes awk to create a RASP-compatable thrust curve for
altitude simulation.

   usage:   mkcurve [-w] <file[.raw]> [<file2[.raw]> <file3[.raw]> ... ]

<file.raw> contains linear measurements from the test stand and
physical info on the motor.  I included sample .raw files ( look
at ht076.raw for a more-or-less complete description of mkcurve
syntax )

There can be as many REM lines as you like to identify the particular
motor and environmental conditions at run-time ( see ht076.raw ;-).

For unix / dos users, the -w directive causes mkcurve to create a
file.eng, otherwise output is to stdout.

Put mkcurve and strwac in your local bin directory and put mkcurve.awk
in your local awklib directory. Edit mkcurve, set varb AwkProg to your
local version of awk|nawk|gawk and set varb AwkLib to point at your local
awk lib directory.

I included a lame bat file, mkcurve.bat for DOS users.

    usage:  mkcurve [ -w ] file [ file ... ]

DO NOT include the .raw in the file name.  For example,

   mkcurve -w ati112

creates file ati112.eng from ati112.raw.  On the other hand,

   mkcurve ati112

spews the output to the screen.

Mac users are SOL, please send me a mac script file if there is
such a thing.

If you have digitrak ( Larry Curcio's excellent altitude simulator
and temporal backtracking system ), then run the .eng file thru
markurve to produce a digitrak-compatable thrust file.  If you don't
have it, digitrak is at

   sunsite.unc.edu:/pub/archives/rec.models.rockets/DIGITRAK/

gawk compiled for dos is at:

   oak.oakland.edu:/pub/simtelnet/gnu/gnuish/gawk300?.zip

gawk compiled for the MAC is at:

   ftp.uwtc.washington.edu:/pub/Mac/Programming/

awk|nawk|gawk is already on unix boxes ;-)

Enjoy!

-- kjh